## Slide 1: HAZMAT
CWO2 E. W. Bertsch
USCG-R

## Slide 2: What is HAZMAT?
49 CFR 171.8: Hazardous material means a substance or material that the Secretary of Transportation has determined is capable of posing an unreasonable risk to health, safety, and property when transported in commerce, and has designated as hazardous under section 5103 of Federal Hazardous Materials Transportation Law (49 U.S.C. 5103).

## Slide 3: What is HAZMAT?
The term includes hazardous substances, hazardous wastes, marine pollutants, elevated temperature materials, materials designated as hazardous in the Hazardous Materials Table (see 49 CFR 172.101), and materials that meet the defining criteria for hazard classes and divisions in part 173 of this subchapter.

## Slide 4: Hazard Classes

## Slide 5: Class 1: Explosives (49 CFR 173.50)
1.1, Mass explosion hazard
1.2, Projection hazard
1.3, Predominantly a fire hazard (minor blast or projection hazard)
1.4, Minor explosion hazard
1.5, Very insensitive explosives
1.6, Extremely insensitive explosives

## Slide 6: Class 2: Gases (49 CFR 173.115)
2.1, Flammable gas
2.2, Non-flammable, non-poisonous compressed gas
2.3, Gases poisonous by inhalation

## Slide 7: Class 3: Flammable/Combustible Liquids
49 CFR 173.120(a), A flammable liquid is a liquid that has a flash point (FP) of not more than 60 degrees Celsius (140 F), or any material in a liquid phase with a FP at or above 37.8 degrees Celsius (100 F) that is intentionally heated and offered for transport or transported in bulk.
49 CFR 173.120(b), A combustible liquid is any liquid not meeting the requirements of any other hazard class that has a flash point above 60 degrees Celsius (140 F) and below 93 degrees Celsius (200 F).

## Slide 8: Class 4: Flammable Solids, Spontaneously Combustible, and Dangerous When Wet Materials
4.1, 49 CFR 173.124(a); Flammable solids including desensitized explosives and self-reactive materials that are thermally unstable and can undergo a strongly exothermic reaction in the absence of oxygen.
4.2, 49 CFR 173.124(b); Spontaneously combustible materials include pyrophoric (liquid or solid that will ignite within 5 minutes of exposure to the air, even in small quantities and without ignition source) materials and self heating (reacts with O2 in the air to generate heat and possible self-ignition and combustion) materials.

## Slide 9: Class 4 (continued):
4.3, 49 CFR 173.124(c); Dangerous when wet materials are any materials that, when in contact with water, are liable to become spontaneously flammable or to give off flammable or toxic gas at a rate greater than 1 L/Kg of the material per hour.

## Slide 10: Class 5: Oxidizers and Organic Peroxides
5.1, 49 CFR 173.127(a), Oxidizer means any material that may, generally by yielding oxygen, cause or enhance combustion of other materials.
5.2, 49 CFR 173.128(a), Organic peroxide means any organic compound containing oxygen (O) and the bivalent (-O-O-) structure and which may be considered a derivative of hydrogen peroxide, where one or more of the hydrogen atoms have been replaced by organic radicals.
  Types A (Forbidden) through G (Non-regulated) with varied degrees of detonation, deflagration, or explosive power based on factors such as confinement, cavitated states, or thermal influence.

## Slide 11: Class 6: Poisonous Materials and Infectious Substances
6.1, Poisonous materials, 49 CFR 173.132(a); are any materials, other than a gas, which is known to be so toxic to humans (or in absence of such data be presumed to be) as to afford a hazard to health during transportation.
6.2, Infectious substances, 49 CFR 173.134(a); are any materials known or reasonably expected to contain a pathogen (bacteria, viruses, parasites, fungi) or other agent such as a protienaceous infectious particle (prion) that can cause disease in either humans or animals.

## Slide 12: Class 7: Radioactive Materials
49 CFR 173.403; means any material containing radionuclides where both the activity concentration and the total activity in the consignment exceed the values specified in the table in 173.436 or values derived according to the instructions in 173.433.

## Slide 13: Class 8: Corrosive Materials
49 CFR 173.136(a); a liquid or solid that causes full thickness destruction of human skin at the site of contact within a specified period of time. A liquid, or a solid that may become a liquid during transportation, that has a severe corrosion rate on steel or aluminum based on criteria in 173.137(c)(2).

## Slide 14: Class 9: Miscellaneous Hazardous Materials
49 CFR 173.140; any material which presents a hazard during transportation but which does not meet the criteria of any of the other hazard classes.

## Slide 15: Applicability of the Hazardous Materials Regulations (49 CFR 171-180)
Federal Hazardous Materials Transportation Law (49 U.S.C. 5101 et seq.) directs the Secretary of Transportation to establish regulations for the safe and secure transportation of hazardous materials in commerce, as the Secretary considers appropriate.
The Modal Agencies have established their own programs to prioritize their inspection activities of transporters of hazardous materials.
  Violations found during carrier audits
  Non-frivolous written complaints
  HAZMAT incident reports
  Other agency referrals and targeting of high risk HAZMAT

## Slide 16: Applicability of the HMR
Interstate, intrastate, and foreign carriers by rail car, aircraft, motor vehicle and vessel.
The representation that a hazardous material is present in a package, container, rail car, aircraft, motor vehicle or vessel.
The manufacture, fabrication, marking, maintenance, reconditioning, repairing or testing of a package or container which is represented, marked, certified or sold for use in the transportation of hazardous materials (49 CFR 171.1(a))

## Slide 17: General Requirements (49 CFR 171.2)
(a) Each person who performs a function covered by this subchapter must perform that function in accordance with this subchapter.
(b) Each person who offers a hazardous material for transportation in commerce must comply with all applicable requirements of this subchapter, or an exemption or special permit, approval, or registration issued under this subchapter or under subchapter A of this chapter. There may be more than one offeror of a shipment of hazardous materials. Each offeror is responsible for complying with the requirements of this subchapter…

## Slide 18: Enforcement of the HMR
Special agents of the Department of Transportation can not be denied reasonable access to those areas that fall within the official scope of their duties. The Secretary has delegated this authority to the Federal Aviation Administration (FAA), Federal Motor Carrier Safety Administration (FMCSA), Federal Railway Administration (FRA), Pipeline and Hazardous Materials Safety Administration (PHMSA), and the United States Coast Guard (USCG).

## Slide 19: Better follow the rules, 49 CFR 171.1(g)
Penalties for noncompliance. Each person who knowingly violates a requirement of the Federal Hazardous Material Transportation Law, an order issued under Federal Hazardous Material Transportation Law, subchapter A of this chapter, or a special permit or approval issued under subchapter A or C of this chapter is liable for a civil penalty of not more than $75,000 for each violation, except the maximum civil penalty is $175,000 if the violation results in death, serious illness or severe injury to any person or substantial destruction of property. There is no minimum civil penalty, except for a minimum civil penalty of $450 for a violation relating to training.

## Slide 20: Criminal Penalties
An individual who willfully violates a provision of the HMR may be fined, under Title 18 U.S.C., up to $250,000, be imprisoned for not more than 5 years, or both; a business entity may be fined up to $500,000.

## Slide 21: Part 176, Carriage by vessel
§176.15 Enforcement; An enforcement officer of the U.S. Coast Guard may at any time and at any place, within the jurisdiction of the United States, board any vessel for the purpose of enforcement of this subchapter and inspect any shipment of hazardous materials as defined in this subchapter.

## Slide 22: Title 33 Navigation and Navigable Waters, Part 6 Protection & Security of Vessels, Harbors, and Waterfront Facilities
§6.04-1 Enforcement. (a) The rules and regulations in this part shall be enforced by the Captain of the Port under the supervision and general direction of the District Commander, Area Commander, and the Commandant. All authority and power vested in the Captain of the Port by the regulations in this part shall be deemed vested in and may be exercised by the District Commander, Area Commander, and the Commandant.
(b) The rules and regulations in this part may be enforced by any other officer or petty officer of the Coast Guard designated by the District Commander, Area Commander, or the Commandant.

## Slide 23: Title 33 Navigation and Navigable Waters, Part 6 Protection & Security of Vessels, Harbors, and Waterfront Facilities
§6.04-7 Visitation, search, and removal. The Captain of the Port may cause to be inspected and searched at any time any vessel, waterfront facility, or security zone, or any person, article, or thing thereon or therein, within the jurisdiction of the United States, may place guards upon any such vessel, waterfront facility, or security zone and may remove therefrom any and all persons, articles, or things not specifically authorized by him to go or remain thereon or therein.

## Slide 24: Title 33 Navigation and Navigable Waters, Part 6 Protection & Security of Vessels, Harbors, and Waterfront Facilities
§6.04-8 Possession and control of vessels. The Captain of the Port may supervise and control the movement of any vessel and shall take full or partial possession or control of any vessel or any part thereof, within the territorial waters of the United States under his jurisdiction, whenever it appears to him that such action is necessary in order to secure such vessel from damage or injury, or to prevent damage or injury to any vessel or waterfront facility or waters of the United States, or to secure the observance of rights and obligations of the United States.

## Slide 25: Title 33 Navigation and Navigable Waters, Part 6 Protection & Security of Vessels, Harbors, and Waterfront Facilities
§6.04-11 Assistance of other agencies. The Captain of the Port may enlist the aid and cooperation of Federal, State, county, municipal, and private agencies to assist in the enforcement of regulations issued pursuant to this part.

## Slide 26: Title 33 Navigation and Navigable Waters, Part 6 Protection & Security of Vessels, Harbors, and Waterfront Facilities
§160.109 Waterfront facility safety. (a) To prevent damage to, or the destruction of, any bridge or other structure on or in the navigable waters of the United States, or any land structure or shore area immediately adjacent to such waters, and to protect the navigable waters and the resources therein from harm resulting from vessel or structure damage, destruction, or loss, each District Commander or Captain of the Port may;

## Slide 27: Title 33 Navigation and Navigable Waters, Part 6 Protection & Security of Vessels, Harbors, and Waterfront Facilities
§160.109 Waterfront facility safety (continued).
(1) Direct the handling, loading, unloading, storage, and movement (including the emergency removal, control and disposition) of explosives or other dangerous articles and substances, including oil or hazardous material as those terms are defined in 46 U.S.C. 2101 on any structure on or in the navigable waters of the United States, or any land structure or shore area immediately adjacent to those waters; and
(2) Conduct examinations to assure compliance with the safety equipment requirements for structures.

## Slide 28: Safety Zones (33 CFR 165.20)
§165.20 Safety zones. A Safety Zone is a water area, shore area, or water and shore area to which, for safety or environmental purposes, access is limited to authorized persons, vehicles, or vessels. It may be stationary and described by fixed limits or it may be described as a zone around a vessel in motion.

## Slide 29: Security Zones (33 CFR 165.30)
§165.30 Security zones. (a) A security zone is an area of land, water, or land and water which is so designated by the Captain of the Port or District Commander for such time as is necessary to prevent damage or injury to any vessel or waterfront facility, to safeguard ports, harbors, territories, or waters of the United States or to secure the observance of the rights and obligations of the United States.
(b) The purpose of a security zone is to safeguard from destruction, loss, or injury from sabotage or other subversive acts, accidents, or other causes of a similar nature:
(1) Vessels,
(2) Harbors,
(3) Ports, and
(4) Waterfront facilities:

## Slide 30: Security Zone

## Slide 31: Liquefied Natural Gas
AKA: Compressed Natural Gas (CNG), Methane, Processed Gas, Sweet Natural Gas, Treated Gas
UN 1972
Class 2.1

## Slide 32: LNG Vessels
Regulated under 46 CFR, Subchapter O, Part 154
USCG verifies compliance by both plan review and physical examination
US standards more stringent than IGC (International Gas Code)
Barges regulated in Subchapter D

## Slide 33: LNG Facilities
USCG regulates facilities in or adjacent to waterway via 33 CFR 127, Subpart B
Department of Energy (DOE)
Federal Energy Regulatory Commission (FERC)
Maritime Administration (MARAD)
Department of Transportation (DOT)

## Slide 34: Questions?